## Slide 1: Openstor 2910
Technical Presentation

## Slide 2
Key Competitiveness: Easy to Use
Hardware
Software
Unified management
Enterprise-level storage capabilities: dual-controller and multi-protocol
Compute: virtualization and container
3 compute nodes and 2 storage nodes
Installation &
deployment
Monitoring management
Intelligent O&M
Edge-cloud synergy*
PC client
Mobile phone
①
②
③
④
⑤
RESTful API
For SMEs, branches, and edges
Cloud O&M
Multi-site management on DME
All-in-one device
Integration of storage, compute, and network resources in 4 U space
Applications
④
Simplified
Ready-to-use and plug-and-play
Simplified connection, requiring no professional O&M personnel
Integrated
Integration of storage, compute, and network resources in 4 U space
Integrated storage + application platform
⑤

## Slide 3
Compute node | Number of nodes | 2 to 3
 | CPU | 1P/2P: C4310, C4314, C4316, C5318Y, C6330, C6346, and C6348
 | Memory | 16 GB/32 GB/64 GB x 16 (1P)/32 (2P)
 | Flex I/O card | Flex I/O card (OCP): I350 2-port GE card; CX4 2-port 10GE card
 | Standard PCIe card | CX4-2 port 10/25GE X550-2 port 10GE I350-2 port GE
 | AI card | T4, Atlas300I PRO
 | Disk | SAN Boot, without system disks
 | Onboard port | 2 x 10GE + 2 x 10GE
Storage node | Storage controller | Two controllers
 | CPU | 28-core 2.6 GHz per controller
 | Memory | 40 GB per controller
 | Onboard port | 2 x 10GE (used as the storage replication port)
 | Internal port | 2 x 25GE + 16 x 10GE
 | Disk in a controller enclosure | 4 SSDs + 6 HDDs
 | Disk enclosure for capacity expansion | 4 U 3.5-inch disk enclosure x 4, or 2 U 2.5-inch disk enclosure x 4
OpenStor 2910 Product Capabilities
Compute node | Software suite | FusionCompute standard or advanced edition
 | Basic capability | Storage passthrough (eVol), VM template, thin provisioning, VM QoS, memory overcommitment, and dynamic resource scheduler (DRS)
 | Reliability | VM HA
 | Security | VM snapshot and clone
 | DR and backup | DR (being planned) and backup (being planned)
 | Network | Distributed virtual switch
 | GPU capability | GPU virtualization and passthrough
Storage node | Software suite | OceanStor OS basic, advanced, and optional packages
 | Basic service | iSCSI, CIFS, and NFS
 | Software for improved efficiency | SmartAcceleration, SmartQoS, SmartVirtualization, and SmartMigration
 | Software for data protection | HyperSnap, HyperClone, and HyperVault
 | Software for DR | HyperReplication, HyperMetro, and quorum server software
Local management | Site deployment | One-click initialization wizard
 | O&M | Automatic inspection, one-click capacity expansion, and one-stop upgrade
 | Monitoring | Device management, resource management, and performance statistics
 | Security | Security certificate, sandbox protection, and rights-based management
Central management | Software suite | DME Data
 | Management capability | Centralized alarm monitoring, VM management, storage resource management, and VM template provisioning
Hardware Capabilities
Software Capabilities

## Slide 4
Key Hardware Components
Onboard disk enclosure
Compute node (standard x86 mainboard)
Storage node (three-in-one control board)
Hardware Architecture
Software Architecture
Network Architecture

## Slide 5
The System Automatically Divides Multiple Network Planes
Management plane: management network plane of the system. It is used for service operations and O&M management of the system.
Storage network: The 10GE direct network is used for SAN Boot and block services.
Switching network: network plane for customer service communication. It supports the TCP/IP protocol and 10GE networking. It shares the same network with the management plane and is isolated by VLANs.
BMC plane: server management IP plane. It uses the GE network and is used for O&M management of server hardware devices.
Storage A
Storage B
iBMC
iBMC
Mirror channel
BMC plane
Management plane
Switching network
Storage network
MetaVision
VRM
iBMC
User VM
vSwitch
...
MetaVision
VRM
iBMC
User VM
vSwitch
...
MCNA
MCNA
Hardware Architecture
Software Architecture
Network Architecture

## Slide 6
bond1
Compute node 2
1822
3
1
4
2
BMC
Compute node 0
1822
3
1
4
2
BMC
Compute node 1
1822
3
1
4
2
BMC
Switch module
SW
bond4
CTE0.A.I10
eth-hns11
CTE0.A.I3
eth-hns7
CTE0.A.I7 eth-hns4
CTE0.A.I8 eth-hns6
CTE0.A.I9 eth-hns10
CTE0.A.P0
eth-hns14
CTE0.A.P1
eth-hns12
CTE0.B.I7
CTE0.B.I8
CTE0.B.I9
BMC
Switch module
CTE0.B.I1
CTE0.B.I3
CTE0.B.P0
CTE0.B.P1
SW
BMC
Storage B
Storage A
CTE0.A.P2
eth-hns8
CTE0.B.P2
CTE0.A.I0
eth-hns3
CTE0.A.MGMT
eth-hns3.2910
CTE0.B.MGMT
CTE0.B.I0
CTE0.A.I4
eth-hns9
CTE0.A.I6
eth-hns15
CTE0.B.I4
CTE0.B.I6
CTE0.B.I5
CTE0.A.I5
eth-hns13
Controller A
mgmt
mgmt
CTE0.A.I1
eth-hns1
CTE0.A.I2
eth-hns5
CTE0.B.I10
eth-hns0
eth-hns2
bond1/4
bond1/4
25GE, storage management network + service network
10GE, internal switching network
GE, management network
10GE, iSCSI and diskless boot network
10GE, connected to the external network
10GE, storage mirroring network
Panel port
bond1
bond1
CTE0.B.I2
Controller B
Complex Networks Are Hidden Inside the System, Simplifying User Networks
Performance
96 Gbit/s physical bandwidth (max. software bandwidth: 40 Gbit/s)
Independent SAN and NAS networks
Onboard 3 x 10GE
Security
VLAN isolation
Independent management and service network ports
Reliability
Dual-plane symmetrical networking
Automatic network switchover in case of a port fault
Compute network
Switchable between BOND1 and BOND4
Storage network
Active-active NAS/SAN networks
Ease-to-use
Switch-free configuration
Access to any compute or storage node through one service line
Access to any compute or storage node through one management line
Hardware Architecture
Software Architecture
Network Architecture

## Slide 7
III. Key Features of OpenStor 2910

## Slide 8: Simplified Management: In-depth Integration Reduces Deployment Duration by 75%
Storage cluster
Virtualization cluster
Hardware
resource
Unified monitoring
Physical device monitoring
VM status monitoring
Monitoring
Maintenance
Resource management
Openstor 2910 DeviceManager
Performance monitoring
Unified upgrade
One-click capacity expansion
One-click inspection
Unified management platform
for one-stop management
Compute
Storage
Network switching
VM
Pre-installation before delivery, and one-click installation and deployment, enabling quick rollout of new services
75%
6 hours
1.5 hours
Free from network planning
Free from system installation
Free from storage configuration
Free from documentation learning
Easy-to-Use
High Efficiency
Security and Reliability
No specialized tools required

## Slide 9
Simplified Site Deployment by Scanning QR Codes with Mobile Phone, Requiring No Professional Skills
eService
Configuring on the cloud
Site deployment by scanning QR codes with mobile phones
Automatic configuration download
Automatic license import
Automatic quality inspection report obtaining
Automatic archive creation on eService
Internet-free device access
Simplified connection
Portable small box, facilitating plug-and-play
Internet-free access, eliminating customers' concerns
Device management IP addresses
Licenses
Others...
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 10
SSD
SSD
SSD
SSD
POOL
LUN
LUN
LUN
OS
Driver
UVP
VM
Economic and efficient
Costs of server system disks and RAID controller cards are spared.
The deduplication and compression features of the storage system can effectively reduce the space occupied by system disks.
System disk space waste is avoided.
High reliability
There are no system recovery difficulties caused by RAID controller card and system disk faults.
Dedicated SAN BOOT multi-path direct-connection network prevents the impact of external network and single-link faults.
Stateless computing
The OS is decoupled from server hardware, and server nodes can be replaced randomly.
Quick recovery
Inherent advantages of enterprise storage are leveraged to protect OS data.
More innovations
Quick host recovery: The lossless snapshot mechanism of the storage system can be used to quickly recover the host OS if the host OS breaks down unexpectedly due to environment or software errors.
In the future, the entire device will support the evergreen feature, avoiding complex system installation and configuration.
Simplified Hardware: No System Disks on Compute Nodes, Implementing Plug-and-Play of Compute Nodes
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 11
Converged SAN and NAS: One System for Multiple Workloads, Improving Efficiency
Block service
Storage pool
File service
RAID 2.0+
  iSCSI/FC
  NFS/CIFS
  Parallel SAN and NAS
Gateway-free
Integrated block and file storage and NAS gateway-free design for 20% lower procurement costs
Parallel architecture
The system provides optimal paths for concurrent access of SAN and NAS to maximize performance.
Healthcare
HIS/PACS
Finance
Government
E-Gov./OA systems
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 12
Distributed Active-Active Architecture for LUNs and File Systems, Implementing Global Resource Sharing and Load Balancing
Controller A
Controller B
Controller C
Controller D
LUN/File system
SAN/NAS client access protocol
LUNs/File systems do not belong to any controller.
The new-gen OceanStor hybrid flash storage, integrated into the OpenStor 2910 solution, uses a distributed active-active architecture:
LUNs/File systems do not belong to any controller. I/O reads from or writes to LUNs are processed by multiple controllers concurrently. Directories of file systems are distributed to all controllers for parallel processing.
Write I/Os are written to the global cache. Read I/Os are hit in the global cache. Cache flushing and prefetch are evenly processed by controllers.
A global pool is created at the back end. LUN space is evenly distributed to the resource pool across controller enclosures, implementing back-end disk space sharing.
LUN/File system I/O requests
Global cache
DHT
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 13
Hot data scenarios
1
Stable read hot data
2
Stable write hot data
8
Time decay-related write hot data
3
Read: alternate change of hot and cold data
4
Time-related:
There is a higher probability that most recently modified data is read-after-write hot data.
LBA
5
7
Time decay-related read hot data
New
Old
Time
6
Overwrite on non-hot data
Logical address-related
Time decay-related
Data exchange platform
①②③④⑤
Check images
⑦⑧
Virtualization
①③②④⑤⑥
Hot Data Is Changeable. How Can We Effectively Use SSDs to Improve Performance?
Write: alternate change of hot and cold data
Stable hot data
Changeable hot data
Changeable hot data in lifecycle
Read-after-write hot data
Tier+cache technology relies on the ROW append write technology and effectively improves hybrid storage performance.
Read performance acceleration
Write performance acceleration
Tier/Cache
Cache
Strongly dependent on algorithm capabilities
Tier
Tier
(ROW append write technology)
Tier
Tier
(ROW append write technology)
Tier
(ROW append write technology)
Tier
(Optimized automatic configuration)
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 14
SmartAcceleration: Innovative Data Layout Algorithm Accelerates Access to All Hot Data and Delivers Flash-like Experience
Eight data acceleration scenarios
Reading hot data from fixed addresses
Reading hot data from unfixed addresses
Writing hot data to fixed addresses
Writing hot data to unfixed addresses
Reading hot data after write
Overwriting non-hot data
Reading hot data with access frequency decaying over time
Writing hot data with access frequency decaying over time
ROW-based large-block sequential writes
Global data write optimization
Cache
Tier
Flexible convergence of heterogeneous media
Optimal cost-performance balance
Global cold and hot data perception
Multidimensional feature learning of neural networks
SmartAcceleration
100% better performance
SmartCache
SmartTier (Write in Place)
SmartTier (ROW)
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 15
SmartAcceleration: ROW-based Large-Block Sequential Writes Solve Random Write Performance Bottlenecks of HDDs
A
B'
B
C
D
E
D'
E'
P1
P2
Data written
Data to be modified
Traditional solution (OceanStor V5)
Write in Place
A
B'
C
D'
E'
P1'
P2'
Data after modification
B
D
E
Snapshot
protection zone
Snapshot
S
S
Snapshot
The write performance is poor when the data to be written is not at the SSD layer.
Write penalty is generated due to overwriting.
Overheads are generated when original data is migrated to protected zones.
Next-gen OceanStor hybrid flash storage, integrated into the OpenStor 2910 solution, row-based large-block sequential writes
A
B
C
D
E
P1
P2
Data written
New data
B'
D'
E'
X1
X2
P1'
P2'
The latest data
N
S
Snapshot
The latest data
N
Small I/Os are aggregated into large I/Os for sequential writes, eliminating HDD bottlenecks.
New data forms a new RAID group and no write penalty is generated.
The original data does not need to be migrated and no overhead is generated.
Resolve all write performance issues of hot data.
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 16
SmartAcceleration: Elastic Tier/Cache Convergence for Optimal Cost-Performance Balance
Traditional hybrid flash storage
Tier/Cache space isolated
Data migration based on access frequency
Pool 1
Pool 2
Disadvantages
The SSD performance layer is exclusively used and cannot be shared across pools.
Caches and tiers are independent, and physical space usage is inefficient.
Data needs to be frequently migrated based on access frequency, affecting performance.
SSD tier
SAS tier
NL-SAS tier
SSD cache
SSD tier
SAS tier
NL-SAS tier
New-gen OceanStor hybrid flash storage
Elastic tier/cache converged
Performance layer
SSD cache/tier
NL-SAS tier
NL-SAS tier
Advantages
Caches and tiers converge into a performance layer, enabling efficient cross-pool sharing.
The cache-to-tier capacity ratio is automatically configured by the system, achieving optimal efficiency.
Data does not need to be migrated across caches or tiers, reducing the impact on performance.
Regular migration
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 17
SmartAcceleration: Adaptive Access Frequency Perception and Prediction Algorithm, Effectively Improving Hot Data Hits
Multi-granularity hot data statistics
Hot data information always occupies 20 bytes of memory.
High hot data granularity would waste memory space, while low hot data granularity would waste capacity space.
Multi-granularity statistics balance accuracy and efficiency.
1 MB
64 KB
8 KB
64 KB
32 KB
1 MB
8 KB
T0
Current
T1
Time
Cold
Hot
Algorithm: predicts
hot data
Performance layer
Advanced prefetch
Hot data prediction based on time sequence
Insufficient response to periodic changes in hot data when judging hot data based on historical access frequency.
Predicts future hot data based on machine learning algorithms, achieving higher accuracy of hot data hits.
Multidimensional associated data prefetch
Associations between data may be related to logical addresses and time.
Prefetch based on continuous addresses has a low hit rate.
Self-learning of multidimensional correlations
Prefetching based on associations has a high hit rate.
HBA address
HBA address
...
...
Timeline
T0
T1
T2
T3
T4
...
...
...
...
Prefetch based on continuous addresses
Prefetch based on associated addresses
Prefetch based on associated times
SAN/Large files
Memory
space
Small I/O
access frequency info.
Small file
access frequency info.
Small file access frequency info.
eliminated in priority
Small I/O access frequency info.
eliminated in priority
Massive small files
Elimination policies of scenario-based access frequency info.
Small I/Os/Large files (in a tree) and small files (in a queue) differ in the structure of access frequency info., and cannot be combined.
When the memory space is insufficient, some info. needs to be eliminated.
The elimination priority is adjusted based on the I/O scenario.
Performance is greatly improved in hybrid workload scenarios.
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 18
SmartAcceleration: Dynamic, Adaptive Data Layout Policy
Aggregated large I/Os delivered to disks
Write
DRAM
SSD performance layer
HDD capacity layer
Cache
Tier
Small I/Os are written into the SSD tier;
Hot read data is overwritten to the SSD tier.
Regular migration
Read
DRAM
SSD performance layer
HDD capacity layer
Cache
Tier
1. Find hot read data in the DRAM.
Admission: Check whether the data is hot enough to be distributed to SSDs.
2. Find hot read data in the SSD cache.
3. Find hot read data in the SSD tier.
Hot data I/O
Miss
Miss
Miss
Admission
Elimination
Read
(including prefetch)
Write I/O distribution
Intelligent access frequency identification algorithm
Intelligent access frequency identification algorithm
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 19
Test equipment: dual-controller, 1 TB cache, 48 NL-SAS HDDs + 4 SSDs
Performance with value-added features enabled
RAID 6
Initial performance
GC
Snapshot
Competitor hybrid flash storage
Huawei OceanStor hybrid flash storage
Competitor hybrid flash storage: 20% to 30% decrease; Huawei OceanStor hybrid flash storage: <10% decrease
Uncompromised Performance (Value-Added Features Enabled)
ROW Architecture
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 20
Performance Improvement Over OceanStor V5
100%
64 KB small file
Reads/Writes: 6:4
2 GB large file;
8 KB small I/O
Reads/Writes: 7:3
8 KB small I/O
Reads/Writes: 7:3
230%
Performance comparison in typical configurations
48 NL-SAS HDDs + 4 SSDs
New-gen OceanStor
hybrid flash storage
OceanStor V5
110%
*Test results from Huawei Lab
Easy-to-Use
High Efficiency
Security and Reliability
180%

## Slide 21
SmartCompression: High Performance and High Reduction Ratio Delivered by Compression + Compaction + Rearrangement
Compression logic optimization
Byte-level compaction
DIF rearrangement
1 KB
3 KB
5 KB
B3
B4
B1
B5
B2
7 KB
9 KB
10 KB
1 KB
3 KB
5 KB
B1
B2
B3
B5
B4
6 KB
Data compression
Data
X
Original data structure
Identifies and rearranges the data integrity field (DIF) values X to ensure data continuity and improve compression efficiency.
Data
X
Data
X
X
Structure after rearrangement
X
X
Structure after compression
Compresses the DIF values.
Data
Data
Data
Data
Data
Data
New X
...
...
...
LZ4: fast compression
Upgraded to
Benchmarks: Linux Mint Debian edition server (Linux version 4.8.0-1-amd64), with a Core i7-6700K CPU @ 4.0 GHz, using lzbench.
Chart: 
| zstd | zlib | quicklz | lzo1x | lz4 | snappy
Ratio | 2.877 | 2.743 | 2.238 | 2.108 | 2.101 | 2.091
Compression Ratios of Mainstream Algorithms
Space wasted by supplementary
Data is aligned by 1 KB and the space wasted by supplementary is not compressed.
Upgraded to
Zstd (high compression ratio)
Write 4 MB data using the 1 KB alignment and compaction technology.
8 KB data blocks
Byte-level alignment achieves space waste of less than 1%.

## Slide 22
HyperLock/WORM: Complies with Industry Regulations to Ensure the Security and Legality of Data Archiving
WORM state transition (OceanStor hybrid flash storage)
Write Once Read Many (WORM) is a data protection technology that allows data to be written only once.
Protected files cannot be modified or deleted after being written.
Enterprise WORM* and Compliance WORM can be selected as required.
Compliance WORM protects data in compliance with SEC Rule 16a-4(f), allowing enterprises to avoid legal risks in confidential file archiving.
The maximum protection period is 30 years. Files can be automatically locked after being written and deleted when the protection period expires.
It is compatible with mainstream NAS backup and archiving software
Clock tampering prevention
WORM
Enterprise mode*
More rights for administrators
Compliance mode
SEC Rule 16a-4(f) compliance
30 years
Max. protection period
Automatic locking and deletion upon expiration
Clock tampering prevention
Initial state
Locked state
Appending state
Expired state
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 23
Secure Snapshot: Protects Important Data Backups from Accidental or Intentional Deletion
LUN/File system
TP
TP+1
TP+2
CDP 0
CDP 1
CDP 2
TP+N
CDP N
...
...
HyperCDP object
Create a secure snapshot.
Rollback
Interval: 3 seconds for LUNs; 15 seconds for file systems
Max. = 60,000 for LUNs
Max. = 4,096 for file systems
In financial scenarios, read-only snapshots are configured for important data and converted into secure snapshots to prevent backups from being deleted accidentally or intentionally. This meets the requirements for long-term secure storage of important data. A retention period can be set for a secure snapshot. The snapshot cannot be deleted within the retention period. After the period expires, it can be deleted manually or automatically.
Secure snapshot:
Either a single secure snapshot or a secure snapshot consistency group (CG) can be created.
HyperCDP objects can be converted into secure snapshots, and HyperCDP CGs can be converted into secure snapshot CGs.
A secure snapshot cannot be deleted before it expires.
The expiration time of a secure snapshot can be extended.
Security snapshots can be automatically deleted after they expire.
Fast recovery:
In the event of a disaster, a non-infected snapshot in the production center is used for recovery.
Minimum recovery granularity: 3 seconds for LUNs and 15 seconds for file systems
Serial port mode:
The security administrator can shorten the protection period of secure snapshots.
The security administrator can delete secure snapshots that have not expired.
The security administrator can change a secure snapshot to a common snapshot.
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 24
NAS Antivirus: Provides Two Virus Scanning Modes and Is Compatible with Multiple Mainstream Antivirus Software
Front-end host
Antivirus server
TCP/IP
Storage
console
DeviceManager
/CLI
NAS file system
Antivirus function
Antivirus engine
Antivirus agent
Antivirus monitoring
OceanStor storage
Antivirus server
On-demand
scanning
On-access
scanning
SMB
file access
SMB
Virus-infected files
Trigger virus scanning and removal.
ShareOpen/
ICAP
Return the scanning and removal result.
NAS antivirus scans storage systems for files infected by viruses.
Support on-demand and on-access scanning modes and provide virus scanning service on demand.
Support both ShareOpen and ICAP interaction protocols.
Support a maximum of 64 antivirus servers at the same time, improving the throughput.
Compatible with mainstream enterprise-level antivirus software such as Symantec Endpoint, Trend Micro, McAfee, Sophos, and Kaspersky.
Easy-to-Use
High Efficiency
Security and Reliability

## Slide 25
IV. Open Platform

## Slide 26
High Compute Performance and NUMA Topology Optimization
VM compute performance improved by 15% to 30%
Scenario: Applies to multi-core services requiring high memory access, ensuring optimal VM memory access performance.
Slow
VM1
No NUMA
No policy control, slow cross-node memory access
Default scenario
HOST
VM1
NUMA scheduling optimization
A CPU preferentially uses the memory on the same node to reduce memory access latency, improve access efficiency, and improve application performance.
NUMA enabled
Fast
MEM
CPU1
CPU2
MEM
CPU3
CPU4
NUMA Node1
NUMA Node2
MEM
CPU1
CPU2
HOST
MEM
CPU1
CPU2
MEM
CPU3
CPU4
NUMA Node1
NUMA Node2
MEM
CPU1
CPU2
Fast
Stability and Reliability
High Efficiency
Security and Trustworthiness

## Slide 27
Huge Page Memory Access Acceleration and Precise QoS Assurance for Compute Performance
  30% higher performance for large-memory applications
    Scenario: Applies to large-memory services, such as Oracle databases.
  Fine-grained resource allocation, ensuring VM compute performance
    Scenario: Resources are reused to the maximum extent to reduce costs when resources are limited.
Traditional 4 KB page table:
A large number of memory page tables exist. The number of page tables cached by the TLB is limited, causing a high miss rate.
1 GB huge page:
A few number of memory page tables exist. CPUs access TLB cache page tables directly with a high hit rate.
...
...
4k
Miss
Cache page table
Address translation
Memory access
Address translation
Memory access
Direct
access
High-speed
cache
TLB
High-speed
cache
TLB
Low speed and multiple times
1G
Huge page memory optimization
CPU quota
Multiple VMs
compete for the CPU resources based on the CPU quota.
CPU reservation
The minimum CPU computing power
available to VMs is precisely controlled.
Memory quota
Multiple VMs
compete for the memory resources based on the memory quota.
Memory reservation
The minimum memory capacity
available to VMs is precisely controlled.
VM
Note: This applies to memory overcommitment scenarios.
Compute resource QoS
Stability and Reliability
High Efficiency
Security and Trustworthiness

## Slide 28
OVS + DPDK, improving network forwarding performance by 6 times
FusionCompute
Physical NIC
(Intel 82599ES, Intel XXV710, and Intel XL710)
VF
VF
VF
VF
...
VM
vNic1
vNic2
Physical NIC
VM 0
NIC driver
DPDK
vNic
Virtualization layer
No kernel-mode forwarding processing is required.
Kernel mode
Virtual switch
EVS process
User mode
User-mode OVS + DPDK
SR-IOV passthrough
The hardware virtualization capability provided by physical NICs is used to mount virtual hardware devices to VMs. The network I/O performance and latency of VMs are close to those of physical NICs.
The Data Plane Development Kit (DPDK) technology is used to accelerate network forwarding, and huge pages and user mode are used to reduce packet copies, improving network forwarding efficiency by a maximum of six times and greatly improving pulse per second (PPS).
Virtual switch
VM 1
Data
channel
vNic
NIC driver
Physical NIC
Kernel-mode OVS
Virtualization layer
Flow table
The OVS technology is used to provide advanced network features such as IP-MAC binding and security groups, implementing fine-grained network QoS control.
Stability and Reliability
High Efficiency
Security and Trustworthiness

## Slide 29
GPU Graphics Acceleration and Atlas-enabled AI Training
Host
VM
VM
VM
vGPU
vGPU
Host
GPU passthrough
GPU virtualization
GPU driver
GPU driver
GPU driver
GPU passthrough and GPU virtualization are supported, improving user experience of high-performance graphics and image applications.
VM
Altas driver
Host
Huawei Ascend Altas 300 AI acceleration is supported, which provides AI processors with the optimal energy efficiency ratio.
GPU acceleration
AI acceleration
Models that support GPU virtualization and passthrough: NVIDIA P4, P40, M60, and V100 GPU; models that support GPU passthrough only: NVIDIA P100 and Atlas 300
Scenarios: engineering drawing, media production, 3D games, GIS, and graphics and video processing
Scenarios: AI inference and training services
Stability and Reliability
High Efficiency
Security and Trustworthiness
Atlas 300 AI accelerator card

## Slide 30
eVol Storage with Automatic Configuration and Storage Offloading, Improving Performance
Scenarios: high I/O and low latency services such as cluster file systems, and video and image processing, automatic service provisioning, high performance of virtualization service operations; computational storage
eVol storage
FusionCompute
LUN
ISCSI/FC
SAN storage device
vs.
VM1
VM2
Virtual disk
VIMS
Virtual disk
Raw device mapping
LUN
LUN
Shortened storage device I/O path, ultimate performance, automatic end-to-end provisioning, and storage offloading
eVol disk
VM2
LUN
LUN
ISCSI/FC
vs.
RESTful
Advantages
Improved performance: Compared with the VIMS solution, the I/O passthrough VM improves the performance by 15%, meeting the requirements of high-performance scenarios in the industry.
Automatic configuration: A simplified storage management solution is provided for customers, reducing six steps for manual configuration and saving 80% manpower.
Storage offloading: The capabilities of value-added storage features in virtualization can be fully utilized.
Benchmarking with competitors: The VMware vVolume benchmarking features are supplemented.
NOF+ technical preparation: Provide basic storage management functions to prepare for the next step of exiting NOF+.
Stability and Reliability
High Efficiency
Security and Trustworthiness

## Slide 31
Comprehensive Protection, Full Control over Security
Platform security
Transmission security
Automatic redirection to HTTPS
TLS encryption
Network plane isolation
Separation of management, service, and storage planes
******
Account password management
Weak password restriction
Brute force attack prevention
Validity period control
Log management
Access with specific permissions
Modification and tampering forbidden
Operation traceability
Permission management
Rights separation
Rights- and domain-based management
Web security
Prevention against cross-site attacks
SQL injection prevention
EulerOS
Host hardening
Tailoring and hardening
System exception detection
Database hardening
Redundant command clearance
Periodic backup
Update
Security patch
Security vulnerability patches are periodically provided on the official website.
Certification key
Custom replacement
VM security
Data storage security
Data isolation
Secure data deletion
Virtualization antivirus
Agentless antivirus
Agent-based antivirus
Network security
Deep packet inspection (DPI)
Firewall
Security group
Inbound and outbound control
Multi-protocol precise control
Host security
Management and O&M
Network
VM security
Stability and Reliability
High Efficiency
Security and Trustworthiness

## Slide 32
V. Solution

## Slide 33
Branch Office Solution
Performance statistics
Alarm management
Unified configuration
Site Management
Mobile app O&M
Partner tenant managed service
DME:
Unified management and O&M of central and branch offices
Device Manager:
single-node integrated management
branch
branch
branch
branch
eService:
cloud-based O&M
Integrated management of storage, computing, and network devices
Virtual Resource Management

## Slide 34
Branch/Center
ISV application appliance
Physical, chemical, biological lab examination
Integration of district elementary education schools
Edge sites of central control stations
Integrated design for small- and medium-sized IC enterprises
Smart campus management
Application emergency takeover
Enterprise document cloud
Internship and practice scenarios
Education
Large enterprise
Supermarket chain
Electric power
Manufacturing
Horizontal solutions
Core services of small- and medium-sized hospitals
Healthcare
Joint Solutions with FusionCompute Ecosystem

## Slide 35
App store
(HIS cloud)
e+
App release
App settlement
Enterprise
Education
Healthcare
Database
Energy
Transportation
Others
Web client
Monitoring
Deployment
Quick deployment | O&M monitoring | One-click starting and stopping services
App
App
App
App
App
App
Server
App client
Web
App
App monitoring
Remote app deployment
App release/settlement
FCV application store (for customers): Local and cloud application stores can be configured, which allows applications to be pulled from the cloud to local devices.
eService application store (for ISV partners): deployed on a public network to establish an HCI application ecosystem. Applications that pass the compatibility certification can be released in the app store. In addition, authorized ISV partners can remotely deploy applications.
DME IQ (for customers): supports remote application monitoring and deployment.
e+ (for frontline/ISV partners): releases products to Smart Configuration Tool (SCT) and settles orders.
App push
App monitoring
App deployment
eService cloud application store:
Ecosystem building: ISV partners can upload and review applications, and bring applications online and offline.
Settlement: third-party software releasing on e+ and order placement from the SCT configurator
Application push: FCV can be interconnected with the cloud application store. Users can download available applications to the local repository.
Remote application deployment: allows ISVs to remotely deploy applications for customers who have purchased the remote application deployment service.
Remote application O&M: application running status monitoring, application monitoring indicator display, and periodic application update information push
Planning: Cloud Application Store for Online and Offline Application Sharing, DME IQ for Remote Application Monitoring and Deployment